PRODUCT RELEASE NOTE

| RELEASE NOTE for Element Manager System v 4.3.0 DATE 07-28-2014 |  | FIRMWARE |
| --- | --- | --- |

©2013 GE MDS LLC., 175 Science Parkway, Rochester, NY 14620 USA

Phone +1 (585) 242-9600, FAX +1 (585) 242-9620, Web: www.gedigitalenergy.com/communications

Element Manager (EM) SW - Version 4.3.0

Build Info:

Version:       4.3.0

Build Date:  08/07/2014

# Introduction

This document describes Software/Firmware engineering development release of the Element Manager Application software (EM).   EM is used as an Engineering tool to Configure and provision GE MDS radio devices.  This tool allows user to connect to a radio device to read or apply configuration file, as well as saving or loading saved configuration file from a PC.

Rev 4.3.0 New Features and Bug Fixes – Since v4.0.0

- New Supported Devices;

  - entraNET AP

    - inherited other IP radios functionalities (ex: Terminal Session, Telnet, Web, etc…)

  - entraNET Remote

    - General Information

    - Configuration Files

    - Firmware Utilities (latest entraNET 900/2400 hardware rev only)

    - Command Line Mode

    - Poller/Responder

    - Ping

- FING – IP Devices Discovery Utility

- Extended SDx Functionalities;

  - Management pages similar to SDx Embedded Web Look-N-Feel

    - Excepts Firmware Reprogramming/Upgrade Utilities

  - Command Line Interface

  - Serial/IP DLINK Interfaces

- Fixed issue with Poller with RTU [10-80] simulator.

Known Limitations/Errata

The following are known issues that exist in this release of the software.

- EM is currently in conflict with a Sprint USB Internet Device plugged in a PC.  If EM cannot start up properly, try removing any such device and then restart EM.

- Certain USB-to-Serial converter may not be compatible when reprogramming entraNET Remote via serial console port connection;

  - TRIPP-LITE KEYSPAN MODEL USA-19HS

- TFTP server currently does not support file transfer requiring more than 2^16 blocks, it will time out because it rolls over from 0 again.   For example, when using TFTP server for Orbit product image, replace the default block size of 512 to 1024 so the number of blocks will be less than 2^16 blocks of data.

- If “Guide” button does not work, try remove older versions of Adobe Readers in your PC and reinstall latest version of Adobe Reader.

- In Command Line Mode, after DIAGNOSTIC CLOSE timeout, it behaves like back spacing.   Work around by entering a CTRL-C character and then ENTER to show command prompt and continue.

- DLINK diagnostic commands is currently limited to 1 Single Hop Intrusive Mode.   In the future, we may add the following enhancements accordingly to customer demands;

  - Non-Intrusive Mode

  - Remote Node to Remote Node (multi-hops) utilizing diagnostic channel open features

- X710, x810, x790 Alarm Sense is reversed according to radio hardware, compared to description in Manuals.

- X710 DLINK Receive Audio Output Level register level value from -1 to -20 dBm will report error due to unresolved x710 radio firmware issue.

- X790 Receiver Muting Level value comparing between saved configuration from Serial and DLINK will report difference.   Serial has value and DLINK does not.

- When connected to a x710 radio unit via DLINK, changing any values in the RTU simulator page will clear the Serial Port Settings -> RX Data Buffer Delay Time to 0 ms (default value).

- Some register values reported from Serial connection vs. DLINK connection may be different – ex: Tx RF Power Output Status <0 dBm from serial, but reports 0 dBm in DLINK.

- X710, x810, x790 HELP page will be filled with appropriate contents in future release.

- Under some rare use case conditions, application service may not properly closes and requires starting Windows  taskmgr to kill the server associated  javaw.exe or javaw.exe *32 processes.

- Under some rare use case conditions, the Adobe AIR local storage may not be properly upgraded from an older version to a new one.   When that happens, Element Manager will not be able to start since the local storage data is corrupted by Adobe AIR run-time upgrade.   The workaround is to search and delete any file preceding by “PrivateEncryptedData” under your local drive.  For examples;

  - D:\Users\220023485\AppData\Roaming\Adobe\AIR\ELS\com.gemds.elementmanager\PrivateEncryptedData

  - D:\Users\220023485\AppData\Roaming\Adobe\AIR\ELS\com.gemds.elementmanager\PrivateEncryptedDatai

  - D:\Users\220023485\AppData\Roaming\Adobe\AIR\ELS\com.gemds.elementmanager\PrivateEncryptedDatak

  - D:\Users\220023485\AppData\Roaming\Adobe\AIR\ELS\com.gemds.elementmanager\PrivateEncryptedDatav